## Slide 1
NPTEL COMPUTER NETWORKS · WEEK 10
Routing Protocols (OSPF & BGP) and ICMP
Course noc26_cs99 — Prof. Neminath Hubballi, IIT Indore
1 OSPF — Parts 01 & 02
2 BGP — Parts 01 & 02
3 ICMP — Parts 01 & 02
Notes: Good morning/afternoon everyone. Today's presentation covers Week 10 of the NPTEL Computer Networks course by Prof. Neminath Hubballi. This week focuses on how routing works in practice across the Internet—covering Intra-AS routing with OSPF, Inter-AS routing with BGP, and network-layer control and diagnostics using ICMP.

## Slide 2
OVERVIEW
Week 10 Lecture Overview
Lecture | Topic | Core Focus
Lecture 1 | OSPF – Part 01 | Scaling routing, Autonomous Systems, Intra-AS routing, OSPF fundamentals & features
Lecture 2 | OSPF – Part 02 | Two-level hierarchy, 4 router roles, 5 packet types
Lecture 3 | BGP – Part 01 | Inter-AS routing, eBGP vs iBGP over TCP port 179, AS-PATH & NEXT-HOP
Lecture 4 | BGP – Part 02 | Hot potato routing, route selection, policy routing, 4 BGP messages
Lecture 5 | ICMP – Part 01 | Error reporting, IP Protocol 1, message structure, Type/Code table
Lecture 6 | ICMP – Part 02 | Error suppression rules, Ping, Traceroute, ICMPv6
Notes: Week 10 is divided into three two-part modules. In Week 9 we studied theoretical Link-State and Distance-Vector algorithms; in Week 10 we see how they are implemented in the real Internet as OSPF and BGP, followed by ICMP for control messages and troubleshooting.

## Slide 3
OSPF · PART 01
Why Do We Need Hierarchical Routing?
Limits of idealized "flat" routing: all routers identical, one flat network
1
Problem 1 — Scale
With billions of destinations, a table entry for every router/host would exhaust router memory, and routing updates would consume all link bandwidth.
2
Problem 2 — Autonomy
Each ISP wants its own routing algorithm and hidden internal topology.
The Solution: Autonomous Systems
Routers are grouped into Autonomous Systems (ASs): routers under the same administrative control.
Each AS has a globally unique
ASN assigned by ICANN regional registries.
Notes: Prof. Hubballi starts OSPF Part 1 by explaining why we cannot treat the entire Internet as one flat graph. First, a flat graph of millions of routers won't scale in memory or convergence time. Second, ISPs want administrative autonomy over their own networks. Both problems are solved by grouping routers into Autonomous Systems, or ASs.

## Slide 4
OSPF · PART 01
Intra-AS vs. Inter-AS Routing
Feature | Intra-AS (IGP) | Inter-AS (EGP)
Scope | Routers within the same AS | Routers across different ASs
Also known as | Interior Gateway Protocol | Exterior Gateway Protocol
Primary goal | Performance (lowest-cost path) | Policy (business rules dominate)
Protocols | RIP, OSPF, IS-IS, IGRP/EIGRP | BGP
Freedom of choice | Each AS admin picks any IGP | All ASs must speak BGP
Notes: Because routers are grouped into Autonomous Systems, routing splits into two levels: Intra-AS routing inside a single AS—where different ASs can run RIP or OSPF—and Inter-AS routing between different ASs, where the entire Internet uses one standard protocol: BGP.

## Slide 5
OSPF · PART 01
OSPF Fundamentals (RFC 2328)
"Open": public specification (unlike Cisco's EIGRP). "Shortest Path First": link-state protocol using Dijkstra.
1
Build the map
Each router builds a complete directed graph of the AS.
2
Flood LSAs
Link-State Advertisements go to all routers in the AS, not just neighbors.
3
When?
On any link change (up/down/cost) and at least every 30 min.
4
Run Dijkstra
Each router computes a shortest-path tree with itself as root.
Transport: OSPF rides directly inside IP datagrams (IP Protocol = 89) — no TCP/UDP; it does its own reliable transfer.
Notes: OSPF is an open-standard Link-State routing protocol. Every router floods Link-State Advertisements to all other routers in the AS—both when link costs change and periodically every 30 minutes—so every router has a complete graph of the AS and runs Dijkstra's algorithm locally. Notably, OSPF runs directly on top of IP using Protocol Number 89.

## Slide 6
OSPF · PART 01
Key Advances in OSPF over RIP
1
Security
Updates can be authenticated (simple password or MD5) so only trusted routers inject routes.
2
Equal-cost multipath
Traffic is split across all equal-cost paths, not just one.
3
Multiple metrics (TOS)
Different link costs per Type of Service, e.g. satellite: high cost for voice, low for bulk transfer.
4
Unicast + multicast
MOSPF reuses the link-state database to build multicast trees.
5
Hierarchy in one AS
A large AS can be partitioned into Areas.
Why it matters
These features make OSPF the preferred Intra-AS protocol for enterprises and ISPs.
Notes: Prof. Hubballi highlights five major advantages embodied in OSPF compared to simpler distance-vector protocols like RIP: MD5 security authentication, equal-cost multi-path load balancing, Type-of-Service specific link weights, multicast extensions via MOSPF, and hierarchical areas.

## Slide 7
OSPF · PART 02
Hierarchical OSPF & The 4 Router Roles
Two-level hierarchy
An AS is split into Areas. Each area floods link-state and computes shortest paths independently. Backbone (Area 0): every area must connect to it; it routes traffic between all other areas.
1
Internal Routers
Wholly inside one non-backbone area; flood and route only within it.
2
Area Border Routers (ABRs)
In a local area and Area 0; summarize area distances to the backbone.
3
Backbone Routers
Do OSPF routing in Area 0 (ABRs and routers wholly in Area 0).
4
Boundary Routers (ASBRs)
Connect to other ASs; learn external routes (via BGP) and inject them into OSPF.
Notes: In OSPF Part 2, we look at how OSPF scales inside a very large AS by dividing it into Areas connected via Area 0, the Backbone Area. Link-state flooding is confined within each area. You must know the four OSPF router roles: Internal Routers, Area Border Routers, Backbone Routers, and AS Boundary Routers.

## Slide 8
OSPF · PART 02
The 5 OSPF Packet Types
Type | Packet | Purpose
1 | Hello | Sent periodically (e.g. every 10 s) to discover neighbors, check liveness, elect a Designated Router on broadcast LANs.
2 | Database Description (DBD) | Exchanges summaries of the link-state database when an adjacency forms.
3 | Link State Request (LSR) | Requests full details of LSAs that are missing or outdated.
4 | Link State Update (LSU) | Carries one or more full LSAs to flood new link-state info.
5 | Link State Ack (LSAck) | Acknowledges LSUs: reliable flooding directly over IP.
Notes: Because OSPF runs directly over IP without TCP, it handles neighbor discovery and reliable flooding using five packet types: Type 1 Hello packets for liveness, Type 2 Database Description, Type 3 Link State Request, Type 4 Link State Update carrying the actual LSAs, and Type 5 Link State Acknowledgment.

## Slide 9
BGP · PART 01
Border Gateway Protocol (RFC 4271)
The standard Inter-AS (exterior) protocol that binds all ASs together. A Path Vector protocol: it carries the whole path of AS numbers, not just a distance.
Three core responsibilities
1
Learn reachability
Obtain subnet reachability from neighboring ASs; each subnet announces its existence to the Internet.
2
Propagate
Spread that reachability to all routers internal to the AS.
3
Choose good routes
Pick routes using reachability information and AS policy.
Notes: Moving to Lectures 3 and 4 on Border Gateway Protocol: BGP is the only Inter-AS routing protocol used on the public Internet. In BGP, routers do not route to individual destination IP addresses; instead, they advertise and route toward CIDR prefixes—or subnets—using a Path Vector approach.

## Slide 10
BGP · PART 01
eBGP vs. iBGP & BGP Message Types
BGP peers exchange routes over semi-permanent TCP connections on port 179.
eBGP (external)
Session between routers in two different ASs, usually directly connected gateways.
iBGP (internal)
Session between routers in the same AS; distributes external prefix reachability inside.
OPEN
Opens a session and authenticates the sender.
UPDATE
Advertises new routes (with attributes) or withdraws old ones.
KEEPALIVE
Keeps the session alive when idle; acknowledges OPEN.
NOTIFICATION
Reports an error and closes the connection.
Notes: Unlike OSPF which runs raw over IP, BGP runs over reliable TCP on Port 179. BGP uses two types of sessions: eBGP between gateway routers of different ASs, and iBGP among routers inside the same AS. All BGP communication uses just four message types: OPEN, UPDATE, KEEPALIVE, and NOTIFICATION.

## Slide 11
BGP · PART 01
BGP Attributes: AS-PATH and NEXT-HOP
BGP Route = Prefix (e.g. 138.16.64/22) + BGP Attributes
AS-PATH
The ASNs the advertisement has passed through (e.g. AS2 AS3). Each AS prepends its own ASN. Loop prevention: a router that sees its own ASN in the path rejects the advertisement.
NEXT-HOP
The IP of the router interface that starts the AS-PATH (the external gateway where the eBGP route entered). Why crucial: it bridges BGP and OSPF; internal routers look up NEXT-HOP in their OSPF table to find the exit interface.
Notes: When a BGP router advertises a CIDR prefix, it attaches attributes—and a Prefix plus its Attributes is called a Route. The two mandatory attributes emphasized by Prof. Hubballi are AS-PATH, which records every AS traversed and prevents routing loops, and NEXT-HOP, which gives the exact border interface IP address so internal OSPF routers know how to forward packets toward that exit point.

## Slide 12
BGP · PART 02
Hot Potato Routing & BGP Route Selection
Hot Potato Routing
A router in AS1 learns prefix X is reachable via gateways 1b and 1c. Rule: forward to the gateway with the smallest intra-AS (OSPF) cost, ignoring the cost beyond it.
"Pass the hot potato out of my AS as cheaply as possible."
Selection order (eliminate until one route is left)
1
Highest LOCAL-PREF
Policy value set by the AS administrator.
2
Shortest AS-PATH
Fewest AS hops among the rest.
3
Closest NEXT-HOP (hot potato)
Minimum intra-AS IGP cost to NEXT-HOP.
4
BGP identifiers
Router IDs break any remaining tie.
Notes: In BGP Part 2, Prof. Hubballi explains how a router chooses among multiple routes to the same prefix. Be careful with the priority order: Hot Potato Routing is Step 3, only used as a tie-breaker after Local Preference (Step 1) and Shortest AS-PATH length (Step 2).

## Slide 13
BGP · PART 02
BGP Policy Routing
Example: multi-homed customer X
Backbone ISPs A, B, C; stub networks W, X, Y. X connects to both ISP B and ISP C. Problem: if X told B it can reach C, B would push huge transit traffic through X. Policy solution: X simply does not advertise a route to C to B. B never learns B→X→C exists, so X carries only its own traffic.
Intra-AS (OSPF)
Single admin → no policy needed → 100% performance.
Inter-AS (BGP)
Independent commercial entities → policy dominates: a longer compliant path beats a shorter non-compliant one.
Notes: Why don't we use OSPF across the whole Internet? Because in Inter-AS routing, commercial policy dominates over shortest-path performance. A multi-homed customer network X connected to two ISPs B and C will refuse to advertise B's routes to C so that X does not become a free transit backbone between two giant ISPs.

## Slide 14
ICMP · PART 01
ICMP: Internet Control Message Protocol (RFC 792)
Companion to IP: hosts and routers use it to exchange network-layer control information.
1
Error reporting
Tells the original source when a datagram hits an error: unreachable net/host/port/protocol, fragmentation needed, TTL expired.
2
Diagnostics / queries
Echo Request & Reply, used by ping.
IPv4 header "Protocol" field
1
ICMP
6
TCP
17
UDP
ICMP sits just above IP: messages travel as the IP payload.
Notes: In Lectures 5 and 6, Prof. Hubballi covers ICMP—the Internet Control Message Protocol. Even though ICMP is considered part of the Network Layer, its messages are actually encapsulated inside IP datagrams with IP Protocol field set to 1. Importantly, ICMP reports errors back to the original sending host, not to intermediate routers.

## Slide 15
ICMP · PART 01
ICMP Message Format & Error Payload
8-byte ICMP header
Type
8 bits
Code
8 bits
Checksum
16 bits
Rest of header
32 bits
Checksum covers the whole ICMP message (1's complement). Rest of header is type-specific (e.g. Ping ID + sequence number).
Error payload = full IP header (20 B) + first 8 bytes of the original IP payload
Why 8 bytes?
The first 8 bytes of a TCP/UDP segment hold the source port, destination port and the sequence number / UDP length, so the source OS can notify the exact application socket that sent the failed packet.
Notes: A classic exam and presentation point from ICMP Part 1 is the payload of an ICMP error message. Whenever a router drops an IP packet and generates an ICMP error, it attaches the dropped packet's IP header plus the first 8 bytes of the IP payload. Why 8 bytes? Because those 8 bytes hold the TCP or UDP source and destination port numbers, letting the sender's OS identify which application process generated the packet.

## Slide 16
ICMP · PART 01
Important ICMP Message Types & Codes
Type | Code | Message | When used
0 | 0 | Echo Reply | Reply to ping
3 | 0 | Dest. Network Unreachable | No forwarding entry for the network
3 | 1 | Dest. Host Unreachable | Final router cannot reach the host
3 | 2 | Dest. Protocol Unreachable | Host lacks the upper-layer protocol
3 | 3 | Dest. Port Unreachable | No app on UDP port (ends Traceroute)
3 | 4 | Fragmentation Required, DF set | Exceeds MTU with DF=1 (Path MTU Discovery)
4 | 0 | Source Quench | Legacy congestion notice (deprecated)
5 | 0–3 | Redirect | Use a better router on the same LAN
8 | 0 | Echo Request | Sent by ping
11 | 0 | TTL Expired | TTL hits 0 (Traceroute hops)
12 | 0 | Parameter Problem | Bad IP header field/option
Notes: Here is the complete table of ICMP Type and Code combinations taught in Lecture 5. The most critical ones to highlight are Type 8 and Type 0 for Ping, Type 11 Code 0 when TTL expires at an intermediate router, and Type 3 Code 3 and Code 4 for Port Unreachable and Path MTU Discovery.

## Slide 17
ICMP · PART 02
When Are ICMP Errors NEVER Generated?
Four rules prevent broadcast storms and feedback loops:
1
Never for an ICMP error
No error about a datagram carrying an ICMP error (queries like Echo Request can trigger one).
2
Never for non-first fragments
Only fragment offset = 0 can trigger an error; later fragments never do.
3
Never for multicast / broadcast
No error for datagrams sent to link-layer or IP broadcast/multicast addresses.
4
Never for invalid sources
Source must identify one host: not 0.0.0.0, loopback 127.0.0.1 or multicast.
Notes: In ICMP Part 2, Prof. Hubballi emphasizes four strict exception rules where routers must NEVER send an ICMP error message. First, never send an ICMP error about another ICMP error, or you risk an infinite loop. Second, only Fragment 0 can trigger an ICMP error because only Fragment 0 contains the TCP/UDP port numbers. Third and fourth, never generate ICMP errors for broadcast/multicast traffic or invalid source IPs.

## Slide 18
ICMP · PART 02
ICMP in Action: Ping, Traceroute & ICMPv6
1. Ping
Tests reachability, RTT and loss.
Source sends
Type 8, Code 0 (Echo Request); destination replies Type 0, Code 0 (Echo Reply).
2. Traceroute
Sends UDP probes to an unlikely port (33434+) with TTL = 1, 2, 3… (3 probes each). Hop n: router drops it and returns Type 11, Code 0 (TTL Expired) with its IP and RTT. At destination: unused port → Type 3, Code 3 (Port Unreachable) → stop.
3. ICMPv6
Merges ICMP, ARP (Neighbor Discovery) and IGMP (Multicast Listener Discovery).
Adds
Type 2: Packet Too Big, since IPv6 routers never fragment.
Notes: Finally, we see how Ping and Traceroute use ICMP. Ping uses Type 8 and Type 0. Traceroute cleverly sends UDP probes to an unused port with TTL=1, 2, 3, and so on. Each intermediate router drops the expired packet and sends back ICMP Type 11 Code 0, while the final destination host replies with ICMP Type 3 Code 3 Port Unreachable, telling Traceroute that it has reached the target. Thank you, and I am happy to take any questions!